## Slide 1: Hinkson Creek Collaborative Adaptive Management (CAM) Process
Addressing Impairments of Hinkson Creek Relating to Low Macro-invertebrate Populations
http://www.helpthehinkson.org/CollaborativeAdaptiveManagement.htm

## Slide 2: Initiation of Hinkson CAM
EPA, DNR, City, County, and University agreed to address Hinkson Impairments through Collaborative Adaptive Management (CAM) in 2011
  CAM is well suited to uncertainties of this situation
  CAM is used in other environmental applications
  This is the first CAM process used to address a situation for which a TMDL is supposed to be issued

## Slide 3: Hinkson CAM includes 3 Groups
Stakeholder Committee
  Made up of local interested parties steer the process
    Private Lands
    Business
    Environmental
    Education
    Local Government
Science Team
  Includes USGS, Department of Conservation, MU, DNR, EPA, Private Consultant
  To advise and make recommendations regarding technical issues
    How to address things that may cause the impairment
    Things to study
    Structure of studies
Action Team
  MS4 Partners (City, County, MU), Boone County Regional Sewer District, MoDOT
  To recommends
    Ways to address things that may cause impairment
    Project Structure
    Project Estimates
    Steering Projects through the 3 main entities (City, County, MU)

## Slide 4: Official CAM Projects
Physical Habitat Assessment
  Assessment of Stream Conditions, Geometry, and Habitat from the mouth at Perche Creek to northeast of Hallsville
    See website above for GIS tool which incorporates findings
Forum Nature Area Level Spreader
  Install a device to spread runoff from ~120 acres over an area of Hinkson Floodplain in Forum Nature Area
    Efficacy is being studied
    Project includes riparian restoration
Information is available at http://www.helpthehinkson.org/CAMProjects.htm

## Slide 5: Official CAM Projects, cont.
Flow and Sediment Study
  Studied flow and sediment yields at 5 sites along Hinkson, from rural to urban
    Sediment Concentration dropped from rural to rural/urban interface
    Concentrations rose from rural/urban interface to outlet
El Chaparral Riparian Restoration
  Restoring riparian vegetation and function to a decommissioned sewer treatment site.
    Work began in 2017
    Construction and Seeding expected to be complete this spring
Additional Sampling of Macro-invertebrates by DNR
  5 years of additional sampling every spring and fall from 2012 to present

## Slide 6: Official CAM Projects, cont.
Various Interpretive and Strategy Tools Produced
  Science Team’s Conceptual Model to help tease-out expected effects of changes in Hinkson Watershed
  Physical Habitat Assessment GIS Tool
  Hinkson Creek at a Glance StoryMap
  Hinkson Virtual Tour
  Summary of Missouri University Master Plan (as it relates to Hinkson Creek)
  Science Strategy Document

## Slide 7: Possible CAM Efforts Under Consideration
Stakeholders Recently Voted to Explore These Actions
  Stream Stabilization Projects
    Halt production of sediment from in-stream
    Replace eroded sections with better habitat
  Additional Macro-invertebrate studies
    Mine existing data for clues regarding cause of impairment
    Do more focused samplings
  Grade Control Program
    Install grade controls to stop channels from incising more
  Riparian Restoration on Public Properties
  Prioritize Various Science Team Suggestions for More Study
  Pursue Funding Through USDA Regional Conservation Partnership Program for rural properties in the watershed

## Slide 8: Projects That Further CAM Goals
MS4 Partners work on many projects which benefit
Hinkson Creek but are not official CAM projects.
Projects for other purposes with stormwater components that the Stormwater Utility agreed to help with in order to further CAM goals
  Compressed Natural Gas Fueling Site
  Lynn Cottages Stormwater Management
  Limerick Lakes Spillway Repair and Water Quality Retrofit
Some projects are primarily to help meet MS4 goals (MS4 Goals and Hinkson Goals Overlap Significantly)
  Ordinances and Design Standards
  Best Management Practice Tracking Database
    Up to 500 Public and Private BMPs
Some projects are going to be done anyway for other purposes but have a potentially good effect on Hinkson Creek
  Sanitary Sewer Projects
  Stadium and Old 63 Intersection Improvements
but are not CAM Projects

## Slide 9: Projects That Further CAM Goals
Native Plantings in Rights-of-Way
  East Broadway Native Plantings in Right of Way
  South Providence Native Plantings in Right of Way
Improved Storage at Landfill East Lake ~ 100 acre drainage area
  Retrofitted Dam so Lake Holds More Water
    Added Channel Protection Detention
    Water also used to help generate gas in Landfill
Stormwater Best Management Practice (BMP) Tracking Database
  Helps ensure private as well as public BMPs are maintained
  ~500 BMPs installed so far in the City
10th and Broadway Improved Tree Planter
  Improvement is using the planter to filter stormwater
  “Suspended pavement” allows the tree to extend roots under the parking area
3M Wetland including wet detention pond for trail project
  More than 100 acres of runoff goes through wetland
  Wet detention on north end helps clean water from commercial area before entering wetland
but are not CAM Projects

## Slide 10: Projects That Further CAM Goals
MoDOT installation of filter along HWY 63 Connector
North Grindstone at Rustic Road Stream Stabilization
  Erosion Threatened Sewer
  Techniques enhance habitat
Sanitary Sewer Inflow and Infiltration Project
  Reduction in Sanitary Sewer Overflows
  Have seen reductions in project areas of 20-60% during rain events
Sanitary Sewer Private Common Collector Elimination Projects
  Helps With Inflow and Infiltration
Stadium and Old 63 Intersection Improvements
Walnut and Ann Bioretention 1
  Bioretention Cell Between Ann Street and Stephens Stables
  Cooperative Project w/ Stephens College
Ordinances and Design Standards
  Redevelopment Rules are particularly pertinent to CAM
but are not CAM Projects

## Slide 11: Projects That Further CAM Goals
City Hall Redevelopment
  Includes Water Quality Improvements
  Also Flood Prevention Detention
7th and Walnut Parking Garage Water Quality Retrofit
5th and Walnut Parking Lot Redevelopment
Ameren Site Cleanup and Conveyance Relocation at Orr St.
  Ameren removed contaminated soil
  Relocated (thus rebuilding) Storm Drain Through Site
Trunk Sewer Main Rehabilitation/Replacement
  Reduces Overflows
  Reduces Inflow and Infiltration
but are not CAM Projects